## Slide 1: Rating of Steel Swing Bridges
Tony Zhang, P.E.
California Department of Transportation
07/30/2019

## Slide 2: Swing Bridge

## Slide 3: From “Analysis of Truss Swing Bridges in BrR” on 2018 BRDBUG Meeting, Jason Miles

## Slide 4: Benefit of End Jacking for Swing Bridges
Deflection Due to Dead Load:

## Slide 5: Benefit of End Jacking for Swing Bridges (Cont.)
Axial Force in Truss Members Due to Dead Load
End jacking increases the rating factors by reducing the forces in critical member due to dead loads.

## Slide 6: End Jacking Application

## Slide 7: Typical Steel Swing Bridges in California
● Steel Plate Girder Bridges
● Steel Truss Bridges
Steel Plate Girder Bridge | Steel Truss Bridge

## Slide 8: Swing Bridge with Partial End Jacking (Steel Plate Girder Bridge)
Bacon Island Road Bridge at Middle River
(Br 29C0108)

## Slide 9: As-Built Plans, Bacon Island Road Bridge

## Slide 10: Typical Sections

## Slide 11: Girder Elevation and Framing Plan

## Slide 12: Jacking Point Details

## Slide 13: Deflection Diagram
Note: Jacking is supposed to recover a portion of the cantilever movement.

## Slide 14: BrR Girder-Floorbeam-Stringer System Model

## Slide 15: Girder End Settlement for End Jacking in BrR Model

## Slide 16: Main Girder Displacement and Shear Diaphragm

## Slide 17: Hinge in Middle & Bending Moment of FloorBeam

## Slide 18: Swing Bridge with Full End Jacking (Steel Plate Girder Bridge)
Bishop Canal Bridge
(Br 29C0114)

## Slide 19: As-Built Plans, Bishop Canal Bridge

## Slide 20: Bishop Canal Bridge (Swing Spans 45.5’ + 23.5’ As-Builts)

## Slide 21: Details of Support at Pier 7 (Pivotal Pier) & Diaphragm

## Slide 22: Jacking/Support Locations at Pier 6 and Pier 8

## Slide 23: Camber Diagram of Swing Spans
Note: Jacking is supposed to recover all the cantilever movement.

## Slide 24: BrR Floorbeam-Stringer System Model (For Bent Cap)

## Slide 25: BrR Girder System Model (For Girders)

## Slide 26: Full End Jacking for this Swing Bridge
The jacking movement compensates the whole cantilever displacement and girder ends.
The swing bridge can be rated as a fixed bridge.

## Slide 27: End Jacking for Swing Truss Bridges in BrR Truss Module

## Slide 28: Limitation in BrR Truss Module
In Current BrR Program, no commands can directly simulate the support settlement or jacking movement at truss ends in BrR Truss Module!

## Slide 29: Methods for Rating Swing Truss Bridges
FE modeling by using CSI Bridge (or other FEM software) and Hand Calculations;
FE Modeling and BrR Truss Module, from Jason Miles’ Presentation “Analysis of Truss Swing Bridges in BrR” on 2018 BRDBUG Meeting.
Proposed Dummy Spring Method in BrR Truss Module only.

## Slide 30: FEM Shortcomings by Using CSI Bridge or other software
1. Time consuming;
2. Both rater and checker need to be familiar with CSI Bridge (or other FEM software);
3. Hard to maintain the FEM files due to the program updating in the future.

## Slide 31
Proposed Method:
Dummy Spring Method

## Slide 32
Note: Rs should be less than 2% of Rp. (The selected stiffness of the spring is supposed much smaller than the stiffness of the cantilever truss system, thus, the force in springs shall be small compared with the truss reactions.)
Step 1. Capture Displacement at Cantilever Ends
(Cantilever Model)

## Slide 33: Step 2. Impose Huge Force at Truss Ends for Targeting Displacement (Continuous Span Model)
Note: Rp should be less than 2% of Rr. The rigid spring with a selected stiffness can only deform at inch level under the imposed big force (much large than forces due to dead loads and live loads on bridges), whereas, the deformation due to dead loads and live load on the bridge is negligible.

## Slide 34: Step 3. Rate the Bridge as a Typical Truss Bridge (Continuous Span Model)

## Slide 35: Example of Dummy Spring Method in BrR Truss Module
Old River Bridge
(Br 29 0045)

## Slide 36: Old River Bridge, Swing Span 128’-0” + 128’-0”

## Slide 37: Elevation View from As-Built Plans

## Slide 38: Design Camber Diagram

## Slide 39: Design Force in Truss Members

## Slide 40: Design Forces and Wedge Reactions from Shop Plans

## Slide 41: Member ID Map
Note: the rigid dummy members will not control rating results, since the rigid dummy members are intentionally selected to take much larger loads than DLs/LLs to get the targeting jacking/wedging movements.

## Slide 42: Δc, Deflection at Cantilever Ends (Cantilever Model)
Spring Member |  |  | Pier 2 | Pier 4 | 
Member Length | L |  | 3 | 3 | ft
Member Area | A |  | 1 | 1 | in^2
Modulus of Elasticity | E |  | 20 | 20 | ksi
Axial Force | P |  | 1.14 | 1.68 | kips
Member Elongation | Δ | P*L/A/E | 2.05 | 3.02 | in
Average Elongation | Δc |  | 2.53 |  | in
Support Reaction Verification | 
Load Case | Rp, kips
Appurtenance | 48
Deck | 170
Stringers | 38
Floor Beams | 26
Truss Self Weight | 94
Super DC | 27
All DL Summary | 403
Max Spring Reaction | 1.68

## Slide 43: Δj, Jacking Distance at End Supports (Field Measurement)
 | Pier 2 (on Deck) |  |  | Pier 4 ( on Deck) |  | 
Unit: inch | Left | Center | Right | Left | Center | Right
Jacking Movement | 1.38” | 1.53” | 1.44” | 1.44” | 1.75” | 0.91”
Average, Each Pier | 1.45” |  |  | 1.36” |  | 
Average, Whole Bridge | 1.41” |  |  |  |  | 

## Slide 44: Δi, Targeting Deflection at Truss Ends (Continuous Spans)
Truss Tip Deflection (Recalled) | Δc |  | 2.53 | in
Jacking Distance (Recalled) | Δj |  | 1.41 | in
Targeting Imposed Movement | Δi | Δc - Δj | 1.12 | in
Spring Length | L |  | 3 | ft
Spring Area | A |  | 1.618 | in^2
Spring Modulus of Elasticity | E |  | 290,000 | ksi
Imposed Force at Truss Tip | P | E*A/L*Δi | 14,600 | kips
Spring Axial Force from BrR Model | P’ |  | 14,655 | kips
Ratio of P vs P’ | % | P’/P | 100.39% | 
Spring Deformation (BrR Model Verification) | Δv | P’*L/A/E | 1.12 | in
Truss End Reaction Verification |  | 
Load Case | Rr, kips | Unit
All DL Summary | 98 | kips
HS20 | 52 | kips
EV3 | 68 | kips
P13 | 161 | kips
Max LL Reaction | 161 | kips
Rigid Spring Constant | 13000 | kips/in
Max LL Displacement | 0.012 | in

## Slide 45: DL Truss Force Verification (BrR v.s. CSI Bridge)
Member Force Comparison, Truss End Movement ONLY |  |  |  | 
 | Force in Mem U5-U6 | Force in Mem U5-L6 | Force in Mem L5-L6 | Cantilever End Movement
 | Kips | Kips | Kips | In
BrR | 108.15 | 9.88 | -109.35 | 1.120
CSI Bridge | 108.93 | 9.78 | -107.73 | 1.120

## Slide 46: LL Truss Force Verification (BrR v.s. CSI Bridge)
Member Force Comparison, One Lane of HS20 Truck, No Impact |  |  | 
 | Force in Mem U5-U6 | Force in Mem U5-L6 | Force in Mem L5-L6
 | Kips | Kips | Kips
BrR | 27.49 | -65.26 | -27.18
CSI Bridge | 27.49 | -65.18 | -27.19

## Slide 47: Rating Summary
Swing Truss Members Only |  |  | 
 | Rating Factor |  | Critical Locations
Design Loading |  | Ton | 
Inventory | 2.06 | 74.07 | U7L7
Operating | 3.44 | 123.70 | U7L7
Legal Rating |  | Posting US Tons | 
Type 3 (25T) | 4.42 | 110.59 | U5L5
Type 3S2 (36T) | 4.78 | 172.04 | U5L5
Type 3-3 (40T) | 5.35 | 214.13 | U5L5
NRL | 2.85 | 113.87 | U5L5
SU4 | 3.80 | 102.54 | U5L5
SU5 | 3.56 | 110.36 | U5L5
SU6 | 3.20 | 111.31 | U5L5
SU7 | 2.99 | 115.84 | U5L5
EV2 | 3.87 | 111.32 | U5L5
EV3 | 2.49 | 106.86 | U5L5
Permit Rating |  |  | 
5 Axle Truck | 2.40 | 146.43 | U5L5
7 Axle Truck | 2.30 | 195.77 | U7L7
9 Axle Truck | 2.30 | 251.04 | U7L7
11 Axle Truck | 2.16 | 287.38 | L6U7
13 Axle Truck | 2.06 | 324.10 | L6U7

## Slide 48: Benefit of Dummy Spring Method
1. It may directly generate BrR load rating summary table for the whole bridge on SQL server;
2. No any time-consuming FE modeling is necessary;
3. The method is straight forward and easy to use;

## Slide 49: Thanks!
Any Questions?