## Slide 1: 3D Analysis with AASHTOWare Bridge Design and Rating

## Slide 2: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 3: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 4: Review of Finite Element Modeling Basics
Beam elements:
Are used for concrete beams, steel girder flanges, and diaphragms
Have six degrees of freedom (DOFs) at each node

## Slide 5: Review of Finite Element Modeling Basics
Shell elements:
Are used for the steel girder web and the deck
Have four nodes with six DOFs at each node
Girder Web
(Shell Element)
(Typ.)

## Slide 6: Review of Finite Element Modeling Basics
Deck-to-beam connection:
Master-slave constraint – used for 3D curved girder systems
Rigid link connection – used for 3D straight girder systems
Connects center of gravity of deck to girder top flange
Deck-to-beam Connection (Typ.)

## Slide 7: Review of Finite Element Modeling Basics
Modeling of reinforced concrete sections in 3D:
Beam elements used for reinforced concrete beam
Shell elements used for deck/top flange
Rigid links used for connection (straight girder)

## Slide 8: Review of Finite Element Modeling Basics
Modeling of prestressed concrete sections in 3D:
Beam elements used for prestressed concrete beam
Shell elements used for deck
Rigid links used for connection (straight girder)

## Slide 9: Review of Finite Element Modeling Basics
Modeling of steel beam with concrete deck in 3D:
Beam elements used for steel girder flanges
Shell elements used for deck and steel girder web
Rigid links used for connection (if straight girder)

## Slide 10: Review of Finite Element Modeling Basics
Dead loads:
Stage 1 – non-composite dead loads
Stage 2 – composite dead loads
Distributed loads are converted to nodal forces
Discretization of model must be sufficient to ensure series of nodal loads accurately represents distributed load

## Slide 11: Review of Finite Element Modeling Basics
Live loads:
Stage 3 – live loads
Applied to influence surface
Location of vehicle selected to produce maximum of desired effect

## Slide 12: Review of Finite Element Modeling Basics
Support conditions:
Free bearings – permit translation in all directions
Guided bearings – permit translation in only one direction, usually either longitudinal or transverse
Fixed bearings – do not permit translation in any direction
For each of these three support conditions, rotation can be provided or limited in many different combinations

## Slide 13: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 14: Review of the Generated Model
Definition of elements for curved structures:
Curvature is represented by straight elements with small kinks at node points
Elements are not curved
Actual Curve
Elements in the model

## Slide 15: Review of the Generated Model
Non-skewed model:
Deck and beam are divided into elements
The software allows user to adjust number of shell elements and target aspect ratio for shell elements

## Slide 16: Review of the Generated Model
Skewed model:
Nodes are defined along the skew

## Slide 17: Review of the Generated Model
Nodes:
Numbers each node of generated model
Defines X, Y, and Z coordinates for each node
The tables on this and the following slides define the model generated based on data entered by the user

## Slide 18: Review of the Generated Model
Master Slave Node Pairs:
Used to define connection between girder and deck for steel curved girders
Master node is in deck
Slave node is along girder top flange
One-to-one correlation between master node and slave node

## Slide 19: Review of the Generated Model
Beam Elements:
Numbers each beam element in the generated model
Defines start node and end node
Also defines reference node
Sta. Ahead

## Slide 20: Review of the Generated Model
Shell Elements:
Numbers each shell element in generated model
Defines Node1 through Node4 for each shell element

## Slide 21: Review of the Generated Model
Supports:
Identifies all support nodes
Defines the following in X, Y, Z directions
Translation state (fixed or free)
Translation spring constant (kip/in)
Rotation state (fixed or free)
Rotation spring constant (in-kip/Deg)

## Slide 22: Review of the Generated Model
Inclined Supports:
Defines constraint type – translational or rotational
Defines X, Y, and Z components of a 10’ line oriented in the direction of constraint (i.e., oriented perpendicular to the direction of allowable movement)

## Slide 23: Review of the Generated Model
Inclined Supports:
Constraints specified in local coordinate system at support
User defines orientation of local coordinate system as either:
Parallel to tangent of member reference line at support
Parallel to specified chord angle from the tangent

## Slide 24: Review of the Generated Model
Member Releases:
Generated to model hinges and pinned diaphragm connections
Provides the following in X, Y, Z directions
Translation release (false or true)
Rotation release (false or true)

## Slide 25: Review of the Generated Model
Load Case:
Each load is identified by load case and load ID
Loads are applied at nodes
Provides the following in X, Y, Z directions
Force (kips)
Moment (kip-ft)

## Slide 26: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 27: Review of the User-Interface for Steel Multi-Girder Superstructure
Superstructure Definitions:
Provides tree structure
Includes each Member and each Member Alternative
Provides navigational tool to access each window
The following slides highlight data that is specific to 3D finite element models

## Slide 28: Review of the User-Interface for Steel Multi-Girder Superstructure
Girder System Superstructure Definition – Definition Tab
Define Horizontal Curvature Along Reference Line
Right
Left
Sta. Ahead

## Slide 29: Review of the User-Interface for Steel Multi-Girder Superstructure
Girder System Superstructure Definition – Definition Tab

## Slide 30: Review of the User-Interface for Steel Multi-Girder Superstructure
Girder System Superstructure Definition – Analysis Tab
Define refined vs. speed
Define Longitudinal Loading and Transverse Loading

## Slide 31: Review of the User-Interface for Steel Multi-Girder Superstructure
Define Bearing Alignments (Tangent or Chord with Chord Angle)
Enter Distance from Reference Line to Leftmost Girder
Summary of Girder Radii
Structure Framing Plan Details – Layout Tab
Applies Bearing Alignment Properties to All Members

## Slide 32: Review of the User-Interface for Steel Multi-Girder Superstructure
Diaphragm Definition
Provide all required diaphragm information

## Slide 33: Review of the User-Interface for Steel Multi-Girder Superstructure
Structure Framing Plan Details – Diaphragms Tab
For a 3D analysis, this load is used only if it is entered, and if it is not entered, the software will determine the dead load based on the Diaphragm Definition

## Slide 34: Review of the User-Interface for Steel Multi-Girder Superstructure
Diaphragm Loading Selection
Select diaphragms for influence surface loading in the 3D analysis

## Slide 35: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 36: Review of How the Analysis is Performed
Analysis Settings
Select 3D FEM (for Design Review or Rating) or 3D FEM-Vehicle Path (for Rating only)

## Slide 37: Review of How the Analysis is Performed
Analysis Settings – Output Tab
Select AASHTO Engine Reports

## Slide 38: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ll learn in this presentation:
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 39: Review of Available Output
List of major sections of output
Model Actions report provides moments and shears
Model, FE Model Graphics, Transverse Loader Patterns available
Select for list of major sections of output

## Slide 40: Review of Available Output
Model Viewer:
Model can be viewed graphically
Model Viewer permits view from many different vantages
Ability to select what portions of model are viewed
Ability to view influence surfaces

## Slide 41: Review of Available Output
User-interface tabular reports:
Output can be viewed in tabular reports
This example presents dead load analysis results
Select for tabular results for dead load effects, live load effects, and ratings

## Slide 42: Review of Available Output
User-interface tabular reports:
This example presents live load analysis results

## Slide 43: Review of Available Output
User-interface tabular reports:
This example presents load rating results

## Slide 44: Review of Available Output
User-interface graphs:
Output can also be viewed as graphs
This example presents dead load and live load moments
Select for graphical results for dead load and live load effects

## Slide 45: Review of Available Output
Specification checks:
Stages 1, 2, and 3 spec checks can be selected at each node
Available for selected method (LFR/LFD or LRFR/LRFD)
Detailed calculations available for each spec check
Select for specification checks for plate

## Slide 46: 3D Analysis with AASHTOWare Bridge Design and Rating
Here’s what you’ve learned in this presentation :
Review of finite element modeling basics
Review of generated model
Review of the user-interface for steel multi-girder superstructure
Review of how the analysis is performed
Review of available output

## Slide 47: 3D Analysis with AASHTOWare Bridge Design and Rating
  Thank you